## Slide 1
So far, we have discarded 3D object detection and only remain 3D Semantic Segmentation (lidar segmentation).
Domain adaptation is still preserved; We train our model with both labeled source data and unlabeled target data and test our model on target_test.
We adopt nearly the same architecture as xMUDA, except for the head part, where xMUDA introduces “Dual Head” but we only use “Vinilla Fusion”. The backbones are the same: UNet for 2D images and SparseConvNet for 3D lidar points.
The segmentation labels we use are released after xMuda. So we have rerun xMUDA with the new labels. See the results.
We have run baseline for our “Vanilla Fusion”. Though seemingly strange, but it has outperformed xMUDA. See the results.

## Slide 2
We have tried to add contrastive losses on both source and target training data. But it doesn’t give us a better result on target_test. This corresponds to config meta “contrast_usa”. See the results.
So at this point we return to contrastive loss on a single domain to check its effectiveness on source_test. This corresponds to config meta “src_ctr_usa”. See the results.

## Slide 3
Source_train
Target_train
Source_test
Target_test
Target_val
Nuscenes Dataset Domain Splits
Two Source-Target pairs
  (USA, Singapore) & (Day, Night)
Two splits on source
  Source_train & Source_test
Three splits on target
  Target_train, Target_test & Target_val
All of the experiments (results shown in tables) up to now are carried on these splits!

## Slide 4
nuScenes-lidarseg dataset 32 classes
foreground 23; background 9; altogether 32
Foreground classes (23) |  |  |  | Background classes (9) | 
1 | animal | 13 | static_object.bicycle_rack | 24 | flat.driveable_surface
2 | human.pedestrian.adult | 14 | vehicle.bicycle | 25 | flat.other
3 | human.pedestrian.child | 15 | vehicle.bus.bendy | 26 | flat.sidewalk
4 | human.pedestrian.construction_worker | 16 | vehicle.bus.rigid | 27 | flat.terrain
5 | human.pedestrian.personal_mobility | 17 | vehicle.car | 28 | static.manmade
6 | human.pedestrian.police_officer | 18 | vehicle.construction | 29 | static.other
7 | human.pedestrian.stroller | 19 | vehicle.emergency.ambulance | 30 | static.vegetation
8 | human.pedestrian.wheelchair | 20 | vehicle.emergency.police | 31 | vehicle.ego
9 | movable_object.barrier | 21 | vehicle.motorcycle | 0 | noise
10 | movable_object.debris | 22 | vehicle.trailer |  | 
11 | movable_object.pushable_pullable | 23 | vehicle.truck |  | 
12 | movable_object.trafficcone |  |  |  | 

## Slide 5
nuScenes Lidar Segmentation Challenge 16 classes
(merge similar classes and remove rare classes)
Lidarseg_class | General_class | Lidarseg_class | General_class | Lidarseg_class | General_class
0/ignore | animal(1) | 1/barrier | movable_object.barrier(9) | 9/trailer | vehicle.trailer(22)
 | human.pedestrian.personal_mobility(5) | 2/bicycle | vehicle.bicycle(14) | 10/truck | vehicle.truck(23)
 | human.pedestrian.stroller(7) | 3/bus | vehicle.bus.bendy(15) | 11/driveable_surface | flat.driveable_surface(24)
 | human.pedestrian.wheelchair(8) |  | vehicle.bus.rigid(16) | 12/other_flat | flat.other(25)
 | movable_object.debris(10) | 4/car | vehicle.car(17) | 13/sidewalk | flat.sidewalk(26)
 | movable_object.pushable_pullable(11) | 5/construction_vehicle | vehicle.construction(18) | 14/terrain | flat.terrain(27)
 | static_object.bicycle_rack(13) | 6/motorcycle | vehicle.motorcycle(21) | 15/manmade | static.manmade(28)
 | vehicle.emergency.ambulance(19) | 7/pedestrian | human.pedestrian.adult(2) | 16/vegetation | static.vegetation(30)
 | vehicle.emergency.police(20) |  | human.pedestrian.child(3) |  | 
 | noise(0) |  | human.pedestrian.construction_worker(4) |  | 
 | static.other(29) |  | human.pedestrian.police_officer(6) |  | 
 | vehicle.ego(31) | 8/traffic_cone | movable_object.trafficcone(12) |  | 

## Slide 6
Chart: LidarSeg Challenge 16 Classes Distribution
| ignore | barrier | bicycle | bus | car | construction_vehicle | motorcycle | pedestrian | traffic_cone | trailer | truck | driveable_surface | other_flat | sidewalk | terrain | manmade | vegetation
Lidarseg Challenge | 340994448 | 9305106 | 141351 | 4604760 | 38104219 | 1514414 | 427391 | 2314727 | 736239 | 4907511 | 15841384 | 316958899 | 8559216 | 70197416 | 70289730 | 178178063 | 122581273

## Slide 7
Previous 10 classes + background
  0. car
  1. truck
  2. bus
  3. trailer
  4. construction_vehicle
Lidarseg_class | General_class | Lidarseg_class | General_class | Lidarseg_class | General_class
10/background | animal(1) | 9/barrier | movable_object.barrier(9) | 3/trailer | vehicle.trailer(22)
 | human.pedestrian.personal_mobility(5) | 7/bicycle | vehicle.bicycle(14) | 1/truck | vehicle.truck(23)
 | human.pedestrian.stroller(7) | 2/bus | vehicle.bus.bendy(15) | 10/background | flat.driveable_surface(24)
 | human.pedestrian.wheelchair(8) |  | vehicle.bus.rigid(16) |  | flat.other(25)
 | movable_object.debris(10) | 0/car | vehicle.car(17) |  | flat.sidewalk(26)
 | movable_object.pushable_pullable(11) | 4/construction_vehicle | vehicle.construction(18) |  | flat.terrain(27)
 | static_object.bicycle_rack(13) | 6/motorcycle | vehicle.motorcycle(21) |  | static.manmade(28)
 | vehicle.emergency.ambulance(19) | 5/pedestrian | human.pedestrian.adult(2) |  | static.vegetation(30)
 | vehicle.emergency.police(20) |  | human.pedestrian.child(3) |  | 
 | noise(0) |  | human.pedestrian.construction_worker(4) |  | 
 | static.other(29) |  | human.pedestrian.police_officer(6) |  | 
 | vehicle.ego(31) | 8/traffic_cone | movable_object.trafficcone(12) |  | 
5. pedestrian 10. background
6. motorcycle
7. bicycle
8. traffic_cone
9. barrier

## Slide 8
xMuda 4 classes + background
  0. vehicle
  1. pedestrian
  2. bike
  3. traffic_boundary
  4. background
Lidarseg_class | General_class | Lidarseg_class | General_class | Lidarseg_class | General_class
4/background | animal(1) | 3/traffic_boundary | movable_object.barrier(9) | 0/vehicle | vehicle.trailer(22)
 | human.pedestrian.personal_mobility(5) | 2/bike | vehicle.bicycle(14) | 1/truck | vehicle.truck(23)
 | human.pedestrian.stroller(7) | 0/vehicle | vehicle.bus.bendy(15) | 4/background | flat.driveable_surface(24)
 | human.pedestrian.wheelchair(8) |  | vehicle.bus.rigid(16) |  | flat.other(25)
 | movable_object.debris(10) | 0/car | vehicle.car(17) |  | flat.sidewalk(26)
 | movable_object.pushable_pullable(11) | 4/construction_vehicle | vehicle.construction(18) |  | flat.terrain(27)
 | static_object.bicycle_rack(13) | 2/bike | vehicle.motorcycle(21) |  | static.manmade(28)
 | vehicle.emergency.ambulance(19) | 1/pedestrian | human.pedestrian.adult(2) |  | static.vegetation(30)
 | vehicle.emergency.police(20) |  | human.pedestrian.child(3) |  | 
 | noise(0) |  | human.pedestrian.construction_worker(4) |  | 
 | static.other(29) |  | human.pedestrian.police_officer(6) |  | 
 | vehicle.ego(31) | 3/traffic_boundary | movable_object.trafficcone(12) |  | 

## Slide 9
Chart: Class Distribution
| vehicle | pedestrian | bike | traffic_boundary | background
usa_train | 7.58 | 0.41 | 0.03 | 0.98 | 90.98
usa_test | 8.86 | 0.23 | 0.02 | 1.12 | 89.78
singapore_train | 3.01 | 0.26 | 0.06 | 0.37 | 96.3
singapore_test | 3.5 | 0.33 | 0.09 | 0.49 | 95.6

## Slide 10
Contrastive learning 10 classes + background
  0. vehicle
  1. pedestrian
  2. bike
  3. traffic_boundary
  4. driveable_surface
Lidarseg_class | General_class | Lidarseg_class | General_class | Lidarseg_class | General_class
10/ignore | animal(1) | 3/traffic_boundary | movable_object.barrier(9) | 0/vehicle | vehicle.trailer(22)
 | human.pedestrian.personal_mobility(5) | 2/bike | vehicle.bicycle(14) | 1/truck | vehicle.truck(23)
 | human.pedestrian.stroller(7) | 0/vehicle | vehicle.bus.bendy(15) | 4/driveable_surface | flat.driveable_surface(24)
 | human.pedestrian.wheelchair(8) |  | vehicle.bus.rigid(16) | 5/other_flat | flat.other(25)
 | movable_object.debris(10) | 0/car | vehicle.car(17) | 6/sidewalk | flat.sidewalk(26)
 | movable_object.pushable_pullable(11) | 4/construction_vehicle | vehicle.construction(18) | 7/terrain | flat.terrain(27)
 | static_object.bicycle_rack(13) | 2/bike | vehicle.motorcycle(21) | 8/manmade | static.manmade(28)
 | vehicle.emergency.ambulance(19) | 1/pedestrian | human.pedestrian.adult(2) | 9/vegetation | static.vegetation(30)
 | vehicle.emergency.police(20) |  | human.pedestrian.child(3) |  | 
 | noise(0) |  | human.pedestrian.construction_worker(4) |  | 
 | static.other(29) |  | human.pedestrian.police_officer(6) |  | 
 | vehicle.ego(31) | 3/traffic_boundary | movable_object.trafficcone(12) |  | 
5. other_flat 10. ignore
6. sidewalk
7. terrain
8. manmade
9. vegetation

## Slide 11
Config Metas:
baseline_usa
src_ctr_usa
only_ctr_usa
  , or
contrast_usa

## Slide 12
Architectures(ours)
UNetResNet34
UNetSCN
Sample img feats
(N, 64)
Lidar feats
(N, 16)
(N, 64+16)
Vanilla Fusion(Baseline)
UNetResNet34
UNetSCN
(N, 64)
(N, 16)
(N, 64+16)
MLP(64, 16)
MLP(16, 16)
seg_loss
contrastive_loss
Vanilla Fusion with contrastive loss

## Slide 13
UNetResNet34
UNetSCN
Dual Head with KL Divergence
Architectures(xMuda)
UNetResNet34
UNetSCN
Single Head without KL Divergence
(N, 64)
(N, 16)

## Slide 14
04/05/2021
contrast_usa_v0/v1 train/val loss curve

## Slide 15
contrast_usa_v0:
= 0.1
batch_size=8
train_src_ctrloss & train_tgt_ctrloss nearly coincide

## Slide 16
contrast_usa_v1:
batch_size=8
train_src_ctrloss & train_tgt_ctrloss nearly coincide

## Slide 17
03/28/2021
src_ctr_usa_v3/v4
03/25/2021
src_ctr_usa_v1/v2
only_ctr_usa_v0/v1

## Slide 18
contrastive loss ablation study on single source domain |  | 
Configs | Source_test (mIOU) | Target_test (mIOU)
src_ctr_usa_v0 (0.01) | 68.42 | 61.14
src_ctr_usa_v1 (0.1) | 68.80 | 59.90
src_ctr_usa_v2 (0.5) | 65.55 | 52.04
src_ctr_usa_v3 (0.3) | 66.44 | 54.68
src_ctr_usa_v4 (1.0) | 63.66 | 52.85
baseline_usa_v1 | 68.01 | 63.74

## Slide 19
src_ctr_usa_v0:
= 0.01
#pts = 1024, # groups = 1
batch_size=8

## Slide 20
src_ctr_usa_v1:
#pts = 1024, # groups = 1
batch_size=8

## Slide 21
src_ctr_usa_v2:
#pts = 1024, # groups = 1
batch_size=8

## Slide 22
src_ctr_usa_v3:
#pts = 1024, # groups = 1
batch_size=8

## Slide 23
src_ctr_usa_v4:
#pts = 1024, # groups = 1
batch_size=8

## Slide 25
tgt_contrast_loss & src_contrast_loss
nearly coincide

## Slide 26
03/24/2021
contrast_usa_v3/v4
src_contrast_usa_v0
03/20/2021
baseline_usa_v1(baseline2_usa)
contrast_usa_v1
03/19/2021
Baseline_usa_v0(baseline1_usa)
Contrast_usa_v0

## Slide 27
USA/Singapore |  | 
 | Config | Target_test (mIOU)
xMUDA | dual head + KL_div 2D+3D | 62.53
xMUDA baseline | single head 2D+3D | 62.10
Vanilla fusion baseline | baseline_usa_v0 (B=4) | 61.57
 | baseline_usa_v1 (B=8) | 63.74
Contrastive loss on both source_train & target_train | contrast_usa_v0 | 52.67
 | contrast_usa_v1 | 61.69
 | contrast_usa_v3 | < 60.00
 | contrast_usa_v4 | < 60.00
Hyperparameters to fine-tune:
(0.1, 0.01, 0.005, 0.001)
Temparature (100, 10, 1, 0.5, 0.1, 0.05)
#pts in each group (64, 256, 1024, 2048) & #groups in each sample
Transformation after representation(Linear, Non-Linear, None)
Optimizers(AdamW, Adam, SGD+Momentum)

## Slide 28
contrast_usa:
batch_size=8
contrast_usa_v3:
#pts = 128, # groups = 8
contrast_usa_v4:
#pts = 2048, # groups = 1
contrast_usa_v0:
#pts = 1024, # groups = 1
contrast_usa_v1:
#pts = 1024, # groups = 1
Meta Config:
Sub Configs:

## Slide 29
baseline_usa_v1:
batch_size=8(the same as xmuda)

## Slide 30
UNetResNet34
UNetSCN
(N, 64)
(N, 16)
(N, 64+16)
Vanilla Fusion(Baseline)
baseline_usa_v0:
batch_size=4

## Slide 31
tgt_contrast_loss & src_contrast_loss nearly coincide
UNetResNet34
UNetSCN
(N, 64)
(N, 16)
(N, 64+16)
MLP(64, 16)
MLP(16, 16)
seg_loss
contrastive_loss
contrast_usa_v0:
= 0.1
batch_size=8

## Slide 32
contrast_usa_v1:
batch_size=8
tgt_contrast_loss & src_contrast_loss nearly coincide

## Slide 33
03/16/2021
Xmuda new baseline (trained with new seg labels)
“Multi-modal Multi-Task fusion Ver2” baseline
Move xMuda network structure to our framework; train vanilla fusion

## Slide 34
xMuda, reproduce results with new seg labels |  |  |  |  |  | 
Train/test | USA/Singapore | Usa/Sng |  | Day/night |  | 
Segmentation(mIoU) | Xmuda (dual head, KL_div) | Baseline (train on source) | Oracle (train on target) | Xmuda | Baseline | Oracle
2D | 57.04 | 54.03 | 70.83 | 49.62 | 38.81 | 39.30
3D | 53.57 | 48.41 | 65.55 | 45.55 | 43.75 | 46.84
2D+3D | 62.53 | 62.10 | 75.40 | 52.99 | 48.63 | 43.39
xMuda, old results showed in paper
(seg label obtained by marking points in bounding boxes)

## Slide 35
Train/test: Usa/Sng | Ver1 (separate encoders for points) | Multi-modal Multi-Task fusion Ver2 (shared encoder for points) |  | 
 | Baseline | Baseline (train on source) | Task_loss + lambda * Contrast_loss (tried a few hyperparameters) | 
 |  |  | Train from scratch | Resume from baseline model
Segmentation (mIoU) | 60.69 | 62.48 | 48.80 | 57.63
Detection (mAP) | 51.29 | 45.02 | 37.15 | 41.59
Xmuda, new seg labels |  |  | 
Train/test Usa/Sng | Xmuda (dual head， KL_div) | Baseline (separate two streams) | Vanilla fusion
2D | 57.04 | 54.03 | 
3D | 53.57 | 48.41 | 
2D+3D | 62.53 | 62.10 | 63.74
Multi-modal Multi-Task fusion Ver2
UNetResNet34
UNetSCN
(N, 64)
(N, 16)
(N, 64+16)
Vanilla Fusion(Baseline)
baseline2_usa